************************ Assumption of Prototype Version **********************

*												       *

*	1) The power delivery structure must be rectangular			       *

*	2) A DC supplier will be automatically attached at node (0,0)	       *

*	3) All drown currents are randomly generated by the "tlm-adi.exe" itself *

*	4) clock period is equal to 0.5 ns							 *

* 													 *

*******************************************************************************

***** Input Circuit File Format *****

nx							# of nodes in x- direction

ny							# of nodes in y- direction

dt							time-step (sec)

T							total simulation time (sec)

n_out							# of output waveforms

posx[0]					\\position of 0'st output-node

posy[0] 							is (posx[0],posy[0])

....

....

posx[n_out-1]					\\position of (n_out-1)'th output-node

posy[n_out-1] 						is (posx[n_out-1],posy[nout-1])

Rx[0][0] Lx[0][0] 		            \\Rs' and Ls' values at the 0th row of

Rx[1][0] Lx[1][0] 					x-direction

Rx[2][0] Lx[2][0]

......

Rx[nx-2][0] Lx[nx-2][0]

Rx[0][1] Lx[0][1]					\\Rs' and Ls' values at the 1st row of Rx[1][1] Lx[1][1]						x-direction

Rx[2][1] Lx[2][1]

......

Rx[nx-2][1] Lx[nx-2][1]

......

......

......

Rx[0][ny-1] Lx[0][ny-1]				\\Rs' and Ls' values at the (ny-1)'th Rx[1][ny-1] Lx[1][ny-1] 				row of x-direction

Rx[2][ny-1] Lx[2][ny-1]

......

Rx[nx-2][ny-1] Lx[nx-2][ny-1]

Ry[0][0] Ly[0][0]					\\Rs' and Ls' values at the 0th column Ry[0][1] Ly[0][1]						 of y-direction

Ry[0][2] Ly[0][2]

......

Ry[0][ny-2] Ly[0][ny-2]

Ry[1][0] Ly[1][0]					\\Rs' and Ls' values at the 1st column Ry[1][1] Ly[1][1] 					of y-direction

Ry[1][2] Ly[1][2]

......

Ry[1][ny-2] Ly[1][ny-2]

......

......

......

Ry[nx-1][0] Ly[nx-1][0]				\\Rs' and Ls' values at the (nx-1)'th

Ry[nx-1][1] Ly[nx-1][1] 				column of y-direction

Ry[nx-1][2] Ly[nx-1][2]

......

Ry[nx-1][ny-2] Ly[nx-1][ny-2]

C[0][0] C[1][0] ..... C[nx-1][0]  		\\caps at the 0th row of x-direction

C[0][1] C[1][1] ..... C[nx-1][1]   		\\caps at the 1st row of x-direction

C[0][2] C[1][2] ..... C[nx-1][2]   		\\caps at the 2nd row of x-direction

.........

.........

C[0][ny-1] C[1][ny-1] C[2][ny-1] .... C[nx-1][ny-1]   \\caps at the (ny-1)'th 										row of x-direction